## Slide 1: CanSat 2015 Critical Design Review (CDR)
Team 4996
Team Phoenix

## Slide 2: Presentation Outline
Introduction – Ruben Perez
System Overview – Ruben Perez
Sensor Subsystem – Maria F. Caceres
Descent Control Design– Patrick Guillaume
Mechanical Subsystem Design – Majlinda Malellari
Communications & Data Handling Subsystem Design – Demetrios Doumas
Electrical Power Subsystem – Joel Annenberg
Flight Software Design – Demetrios Doumas
Ground Control System Design – Demetrios Doumas
CanSat Integration and Testing – Sakif Chowdhury
Mission Operations & Analysis – Ruben Perez
Management – Ruben Perez
Conclusions – Ruben Perez
Presenter: Ruben Perez

## Slide 3: Introduction
Ruben Perez

## Slide 4: Team Organization
Presenter: Ruben Perez
CanSat Team Mentor:
Caitlin Marsh
Mechanical Systems:
Majlinda M.
Faculty Advisor: Y. Andreopoulos
Sensor Systems: Maria C.
Communication & Data Handling:
Demetrios D.
CanSat Integration & Testing:
Sakif C .
Management: Ruben P.
.
2015 CanSat Team:
PHOENIX
Team Leaders:
Ruben P.
Mission Operations & Analysis: Ruben P.
Electrical Power System:
Joel A.
Descent Control:
Patrick G.

## Slide 5: Acronyms
A– Analysis
CDR – Critical Design Review
CONOP – Concept of Operations
D – Demonstration
DCS – Descent Control System
FSW – Flight Software
GCS – Ground Control Station
HW – Hardware
HWR – Hardware Review
I – Inspection
LCO – Launch Control Officer
PDR – Preliminary Design Review
PFB – Pre Flight Briefing
PFR – Post Flight Review
RSO – Range Safety Officer
SOE – Sequence of Events
T – Test
TBD – To Be Determined
TBR – To Be Resolved
VM – Verification method
Presenter: Ruben Perez

## Slide 6: Systems Overview
Ruben Perez

## Slide 7: Mission Summary
BASE MISSION SUMMARY
  Mass: 600 grams +/- 10
  Dimensions: 125mm x 310mm cylindrical
  Apogee Deployment at 600m
  Payload separation from container at 500m
  Passive helicopter/auto-gyro recovery
  Stabilize and descend properly at a minimum altitude of 300m
  Payload Descent rate must be <10m/s and >4m/s
  Payload lands a large hen egg intact
SELECTABLE OBJECTIVE REQUIREMENTS
  Three-axis accelerometer to measure the stability and angle of descent of the payload during descent
  Easier to implement with our CanSat configuration
Presenter: Ruben Perez

## Slide 8: Summary of Changes Since PDR
Presenter: Ruben Perez
Electrical System Changes
  Using LSM303 (accelerometer and magnetometer) instead of ADXL345
  Chrono Dot
Mechanical System Changes
  No changes

## Slide 9: System Requirement
Presenter: Ruben Perez
ID | Req. No | REQUIREMENT
MR-01 | 1 | Mass: 600 +/- 10 grams (CanSat + container + all descent control devices)
MR-02 | 3 | Dimensions: Container must fit in cylindrical payload section of 125mm x 310mm
MR-03 | 4 | Container must use passive descent control system
MR-04 | 5 | Container must not have sharp edges
MR-05 | 6 | Container must be a florescent color, pink, or orange
MR-06 | 9 | CanSat will deploy from rocket payload section
MR-07 | 10 | CanSat will deploy from the rocket payload section
MR-08 | 11 | Use Helicopter recovery system
MR-09 | 12 | All descent control device attachments must survive 50 Gs of shock
MR-10 | 14 | All electronics must be enclosed and shielded from the environment except for sensor
MR-11 | 15 | All structures must be built to survive 15 Gs acceleration

## Slide 10: System Requirement Cont’d
Presenter: Ruben Perez
ID | Req. No | REQUIREMENT
MR-12 | 16 | All structures shall be built to survive 30 Gs of shock.
MR-13 | 18 | All mechanisms must be capable to maintain their configurations under all forces
MR-14 | 19 | Mechanisms shall not use pyrotechnics or chemical
MR-15 | 21 | During descent, the Science Vehicle shall collect and telemeter air pressure, outside and inside air temperature, flight software state, battery voltage, and bonus objective data.
MR-16 | 22 | CanSat will transmit telemetry data every one second
MR-17 | 24 | 900 MHz XBEE Pro radio will be used
MR-18 | 25 | XBEE NETID/PANID set to the team number
MR-19 | 26 | XBEE radio shall not use broadcast mode
MR-20 | 27-28 | The Science Vehicle shall have a video camera installed and recording the complete descent from deployment and landing and include time stamp on the video.
MR-21 | 29 | Science Vehicle descent needs to <10m/s, but >4m/s

## Slide 11: System Requirement Cont’d
Presenter: Ruben Perez
ID | Req. No | REQUIREMENT
MR-22 | 30 | During descent, the video camera must not rotate. The image of the ground shall maintain one orientation with no more than +/- 90 degree rotation.
MR-23 | 31 | Budget: $1000
MR-24 | 33-34 | Telemetry must be display in real time and engineering unit during descent
MR-25 | 35 | Teams shall plot data in real time during flight on the ground station computer.
MR-26 | 36-37 | The ground station shall include one laptop computer, xbee radio and ah and held or table top antenna. Ground station shall be portable.
MR-27 | 38 | The Science Vehicle shall hold one large raw hen’s egg which shall survive launch, deployment and landing.
MR-28 | 40 | The CanSat flight software shall maintain and telemeter a variable indicating its operating state.
MR-28 | 42 | Include an easily accessible power switch which does not require removal from the container for access.

## Slide 12: System Concept of Operations
Presenter: Ruben Perez
Pre launch
Preflight briefing
Integrate CanSat into Payload
Rocket Launched
CanSat will rest in payload envelope
Rocket is launched
CanSat Deployment
600m altitude the CanSat is deployed
Data will be received for the following
The mechanical & electrical components will be placed into the CanSat
Receive telemetry
altitude,
pressure
temperature data.

## Slide 13: System Concept of Operations Cont’d
Presenter: Ruben Perez
PAYLOAD SEPERATES FROM CONTAINER
At 500m altitude the payload will separate from the container
This is where the Autorotative blades are deployed
POST-FLIGHT
At this stage the payload will be at 0m altitude.
The egg will be checked to determine if it survived.
The payload will be located
The CanSat should stabilize at a minimum of 300m.
Descent rate must be <10m/s and >4m/s

## Slide 14: Physical Layout Full Assembly
Presenter: Ruben Perez
Container
Science Vehicle
Release Mechanism
11.5 in
8.0 in

## Slide 15: Physical Layout Science Payload
Presenter: Ruben Perez
4.7 in
4.0 in
8.0 in
2.3 in
0.72 in
3.34 in
1.08 in
1.22 in
Descent System
Release Mechanism
Camera
Egg Container
PCB

## Slide 16: Launch Vehicle Compatibility
In order to test the fit of all components, tubing of inner diameter equal to that of the max required Container diameter will be purchased
  The Payload will fit inside a double open-ended cylindrical tube: the Container
    The container will have a diameter close to the inner diameter of the rocket () with enough space to prevent the science payload from getting stuck because of friction.
    < (Rocket inner diameter)
Presenter: Ruben Perez

## Slide 17: Sensor Subsystem Design
Maria F. Caceres

## Slide 18: Sensor Subsystem Overview
CanSat 2015 CDR: Team 4996 (Phoenix)
Presenter: Maria F. Caceres
CanSat Sensor System
Pressure Sensor
Altitude Sensor
3-Axis Accelerometer
Required Sensors
Temperature Sensors
Inside Temperature
Outside Temperature
Payload Sensors
Secondary Sensors
Luminosity Sensor
Magnetometer
ChronoDot Clock

## Slide 19: Sensor Subsystem Overview
CanSat 2015 CDR: Team 4996 (Phoenix)
Presenter: Maria F. Caceres
Sensors | Model | Description | Placement Location
Altitude Sensor | BMP180 | Provides barometric (altitude derived from barometric measurements) and inside temperature measurements | Payload
Temperature Sensor | TMP36 | Provides the outside temperature measurement. | Payload
3-Axis Accelerometer + Magnetometer Sensor | LSM303 | The 3-axis accelerometer measures stability and angle of descent (objective), while the magnetometer measures magnetic field (in our case, North). | Payload
Camera | Spycrushers Keychain Camera | This camera comes with a time stamp and will record a video during descent. | Payload
Luminosity Sensor | TSL2591 | Its precision allows for exact lux calculations that would come in handy for the flight software. | Payload
Clock | ChronoDot Clock | The Chronodot is an extremely accurate clock that would be used as our mission time recorder in case of a reset. | Payload

## Slide 20: Sensor Changes Since PDR
CanSat 2015 CDR: Team 4996 (Phoenix)
Presenter: Maria F. Caceres
Change | Reason
Accelerometer (from ADXL345 to LSM303) | The LSM303 is a 2-in-1 sensor (accelerometer + magnetometer) which helps saving space. The addition of the magnetometer is for camera stability.
Addition of a clock (ChronoDot) | The clock in the Arduino would not survive in case of a reset.

## Slide 21: Sensor Subsystem Requirements
CanSat 2015 CDR: Team 4996 (Phoenix)
ID | Req. No | REQUIREMENT
SSR-01 | 21 | During descent, the Science Vehicle shall collect and telemeter air pressure (for altitude determination), outside and inside air temperature, flight software state, battery voltage, and bonus objective data (accelerometer data and/or rotor rate).
SSR-02 | 22 | The Science Vehicle shall transmit telemetry at a 1 Hz rate.
SSR-03 | 23 | Telemetry shall include payload mission time with one second or better resolution, which begins when the payload is powered on.
SSR-04 | 27 | The Science Vehicle shall have a video camera install and recording the complete descent from deployment to landing. The video recording can start at any time and must support up to one hour of recording.
SSR-05 | 28 | The video camera shall include a time stamp in the video. The time stamp must work from the time of deployment to the time of landing.
SSR-06 | 40 | The CanSat flight software shall maintain and telemeter a variable indicating its operating state. In the case of processor reset, the flight software shall re-initialize to the correct state either by analyzing sensor data and/or reading stored state data from non-volatile memory. The states are to be defined by each team. Example states include: PreFlightTest(0), LaunchWait(1), Ascent(2), RocketDeployment(3), Stabilization(4), Separation(5), Descent(6), and Landed(7).
Derived from Bonus |  | Use a three-axis accelerometer to measure the stability and angle of descent of the Science Vehicle during descent.
Presenter: Maria F. Caceres

## Slide 22: Altitude Sensor Summary (Payload)
  Altitude Sensor for Payload
  Data processing:
  Processed using:
    Altitude = 44330*(1-(p/1013.25)1/5.255 (from datasheet)
  Pressure processed using Adafruit_BMP085_Unified-master
Sensor Model Adafruit BMP180 | 
Voltage Operation | 3V - 5V
Pressure range | 300hPa – 1100hPa
Altitude range | 9000m to - 500m
Absolute Accuracy | ±2.5hPa
Presenter: Maria F. Caceres

## Slide 23: Air Temperature Sensor Summary
CanSat 2015 CDR: Team 4996 (Phoenix)
Temperature Sensor
Data processing:
  Processed using:
    Temp in °C = [(Vout in mV) - 500] / 10 (from datasheet)
Sensor Model Adafruit TMP36 | 
Voltage Operation | 2.7V - 5.5V
Temperature range | -40ºC to 125ºC
Output Scale factor | 10 mV/ºC
Precision | 0.1 ºC
Presenter: Maria F. Caceres

## Slide 24: Camera Summary
CanSat 2015 CDR: Team 4996 (Phoenix)
Camera
Presenter: Maria F. Caceres
Spycrushers Car Key Chain Spy Camera Keychain SpyCamera | 
Video Resolution | 720x480
Video Format | AVI
Video Frame Rate | 30±1 fps
Time Stamp | Processed on board, no further processing required
Recording medium | On board SD card writer

## Slide 25: 3-Axis Accelerometer Sensor Summary
CanSat 2015 CDR: Team 4996 (Phoenix)
  3-Axis Accelerometer Sensor for Container
Presenter: Maria F. Caceres
Sensor Model Adafruit LSM303 | Adafruit ±16g Accelerometer + Magnetometer
Full scale range (Accelerometer) | ±16Gs
Accuracy (Accelerometer) | ±10%
Full scale range (Magnetometer) | ±1.3Gs to ±8.1Gs
Accuracy (Magnetometer) | ±10%

## Slide 26: Descent Control Design
Patrick Guillaume

## Slide 27: Descent Control Overview
Descent control is used in both the Container and Payload components of the CANSAT:
  Container: Drag by Parachute
  Payload: Auto-gyro system using Carbon fiber blades
CANSAT Section | Control Scheme | Descent Required | Dependencies | Components | Configurations
Container | Parachute | N/A | -Air Flow -CANSAT mass -Parachute Area | -Kevlar string -Ripstop Nylon -Swivel | Upon separation from the rocket, the container’s parachute will deploy, allowing the CanSat to descend at a controlled rate.
Payload | Auto-gyro | 4m/s<v<10 m/s | - Air Flow - CANSAT mass - Rotor Area - Angle of attack | -Carbon-Fiber propellers -Torsion Springs -Ball bearing | Upon release from container, propellers will fold out and will start to rotate due to air flow
Presenter: Patrick Guillaume

## Slide 28: Descent Control Overview (Cnt’d)
1) Altitude = 600 m
Ejection charge deploys CANSAT
from bay as well as nose
cone at apogee. Each has its own
descent control system.
2) Altitude = 600500m
CANSAT (C+P) descends
via parachute at a predicted rate of 10.7 m/s
Presenter: Patrick Guillaume

## Slide 29: Descent Control Overview (Cnt’d)
3) Altitude = 500 m
CANSAT P deploys blades. CANSAT C Still attached to parachute. Blades open up cache some air and start to rotate providing a net upward force for a terminal velocity in the range 4m/s<Vter<10m/s
4) Altitude = 500 m to 0 m
CANSAT P continues to descend with blades and comes in contact with ground. C lands with parachute.
Presenter: Patrick Guillaume

## Slide 30: Descent Control Changes Since PDR
No changes since PDR
Prototype not yet tested
  Reason: delay in acquiring materials due to funding
Presenter: Patrick Guillaume

## Slide 31: Descent Control Requirements
Presenter: Patrick Guillaume
ID | Req. No | REQUIREMENT
DCSR-01 | 4 | The Container shall use a passive descent control system. It cannot free fall. A parachute is allowed and highly recommended. Include a spill hole to reduce swaying.
DCSR-02 | 10 | The Container or Science Vehicle shall include electronics and mechanisms to determine the best conditions to release the Science Vehicle based on stability and pointing. It is up to the team to determine appropriate conditions for releasing the Science Vehicle.
DCSR-03 | 11 | The Science Vehicle shall use a helicopter recovery system. The blades must rotate. No fabric or other materials are allowed between the blades
DCSR-04 | 12 | All descent control device attachment components shall survive 50 Gs of shock.
DCSR-05 | 13 | All descent control devices shall survive 50 Gs of shock.
DCSR-06 | 29 | The descent rate of the Science Vehicle shall be less than 10 meters/second and greater than 4 meters/second

## Slide 32: Container Descent Control Hardware Summary
Container Descent | 12’’ Parachute
Color | Neon pink
Descent Control Capability (CanSat weight: 660g) | ≈11 m/s
Weight | ≈3g
Cost | $10
Preflight Review Testability | Will be tested using object of similar mass
Shock Force Survival (withstand 30Gs) | Kevlar thread (tensile strength: 3620 MPa) Swivel clip (able to survive 160kg pull )
DCS Connections | Follows DCS rules
Only passive components used: Parachute, Swivel clip
Color selection: Make apparatus stand out
Key considerations:
          Parachute size
          Attachment method
Presenter: Patrick Guillaume

## Slide 33: Payload Descent Control Hardware Summary
Only Passive components: Auto-gyro blades and rotor
Key Considerations:
    Blade Profile Blade Material
    Blade Dimensions Number of Blades
Payload Descent | Auto-gyro
Profile | SG6043
Material | Carbon Fiber
Size | Blade Length: 6in
Color | Black
Weight | ≈64g
Trigger | Blades deploy when released from C
Preflight Review Testability | Decent system will be tested in wind tunnel
Survivability (30Gs) | Awaiting Testing
DCS Connections | Follows DCS rules
Presenter: Patrick Guillaume

## Slide 34: Payload Descent System
Blade Length: 6in
Material: Carbon-Fiber
Presenter: Patrick Guillaume

## Slide 35: Descent Rate Estimates (CanSat)
  Calculations used for CANSAT (C+P) Descent
  CanSat descent will be dictated by the carrier parachute
  Approximate CANSAT descent rate can be determined from the following equation:
  With:
  Parachute Diameter
  Coefficient of Drag:
  CanSat Mass:
  Gravitational acceleration:
  Air density:
  From this we find:
Presenter: Patrick Guillaume

## Slide 36: Descent Rate Estimates (Container)
  Calculations used for Container Descent
  Container descent (after payload deploys) will be dictated by the carrier parachute
  Approximate Container descent rate can be determined from the following equation:
  With:
  Parachute Diameter
  Coefficient of Drag:
  Container Mass:
  Gravitational acceleration:
  Air density:
  From this we find:
Presenter: Patrick Guillaume

## Slide 37: Descent Rate Estimates
CanSat 2015 CDR: Team 4996 (Phoenix)
37
AutoGyro requires asymmetric airfoil SG-6043 Blade Profile
The blades are at a negative angle of attack relative to the rotor disk the air moving up through the rotor captures energy like a wind turbine.
Rotational Energy is dissipated through the generation of aerodynamic lift by the blades.
Cannot solve it analytically. Numerical approximation is required
Presenter: Patrick Guillaume

## Slide 38: Descent Rate Estimates
CanSat 2015 CDR: Team 4996 (Phoenix)
38
2 softwares used: Fluent and Matlab
Fluent: Simulations run in Fluent to determine range of Cd and Cl values at various Reynold’s number and angle of attacks
    Assumptions:
            No crosswind
            Steady flow
            Constant air density
            Constant dynamic viscosity
            Constant air pressure
Matlab: Matlab code estimates velocity on impact with ground
    Assumptions:
            No crosswind
            Constant density
Solving equations
Presenter: Patrick Guillaume

## Slide 39: Descent Rate Estimates
CanSat 2015 CDR: Team 4996 (Phoenix)
39
Fluent
Inputs for Fluent:
      x and y component of velocity for given Reynold’s number
      x and y components of local Cd and Cl values for given angle of attack
Outputs for Fluent:
      Average Cd and Cl values
Results:
Value ranges
      Cd:(0.00194-1.32)
      Cl: (-0.268 - 1.321)
Presenter: Patrick Guillaume

## Slide 40
Velocity Contour Plot
Presenter: Patrick Guillaume
Descent Rate Estimates

## Slide 41
Velocity Vector Plot
Presenter: Patrick Guillaume
Descent Rate Estimates

## Slide 42: Descent Rate Estimates
Matlab
Algorithm:
  CD and CL values used to calculate Forces on differential segments of the blade
  Forces are then integrated along the length of the blade
  Forces are broken into Tangential (Rotational) and Vertical components
  Vertical and Angular accelerations are computed
  Velocities for the next time step are computed
  Process is repeated until terminal velocity is reached
Output:
  Approximate terminal velocity obtained 4.3 m/s
  Time to reach terminal velocity: 18s
Presenter: Patrick Guillaume

## Slide 43: Mechanical Subsystem Design
Majlinda Malellari

## Slide 44: Mechanical Subsystem Overview
Presenter: Majlinda Malellari
Material Selection
Container and Science Vehicle: Kevlar and Fiberglass
Hub and connectors: Nylon and ABS plastic
Egg Protection: Cardboard
Egg Protection Mat: Polystyrene
Container
Science Vehicle
Descent System
PCB
Egg Protection
Release Mechanism
Camera
Descent Mount
Parachute Link

## Slide 45: Mechanical Subsystem Changes Since PDR
There were no changes made since the PDR

## Slide 46: Mechanical Sub-System Requirements
Presenter: Majlinda Malellari
ID | Req. NO̊ | Requirement
MSR-01 | 1 | Complete mass of CanSat will be 600 grams +/- 10 grams (without the egg)
MSR-02 | 2-3 | The Science Vehicle shall be completely contained in the container. The container shall fit in the envelope of 125 mm x 310 mm.
MSR-03 | 4-6 | The container shall use a passive descent system (ex. parachute). No sharp edges on the Container and the body shall be a florescent color.
MSR-04 | 11 | The Science Vehicle shall use a auto-gyro recovery system. No fabric can be used between the blades.
MSR-05 | 12-13 | All the descent control device attachment components shall survive 50 Gs od shock.
MSR-06 | 15-16 | All the structures shall be built to survive 15 Gs acceleration, and 30 Gs of shock.
MSR-07 | 18 | All mechanism shall be able to maintain their configuration under all forces.
MSR-08 | 19 | No pyrotechnics or chemicals allowed.
MSR-09 | 31 | Cost of the CanSat shall be under $1000.

## Slide 47: Egg Protection Trade & Selection
Presenter: Majlinda Malellari
Egg Protection (EP) Egg is strongest when force is applied along higher vaulted arc Test using a statistical approach to determine best overall solution. We chose Polystyrene because it is easy to manufacture, and it is light weight. |  | Elastic Support |  | Oobleck |  | Polystyrene | 
Criteria | Weight | Rating | Reason | Rating | Reason | Rating | Reason
Integration | 30% | 3 | Suspended fabric pouch | 2 | Requires water tight container | 4 | Egg crate foam cut to size
Damping Effect | 50% | 4 | Compresses egg along main arcs | 4 | Highly viscous | 4 | Spreads force over entire surface
Size/Mass | 20% | 4 | Lightweight fabric and elastic | 2 | Avg size, very heavy | 4 | Large volume & lightweight
Total Score | 100% | 3.7 |  | 3.6 |  | 4 | 
Rank |  | 2 |  | 3 |  | 1 | 
Decision |  | DECLINE |  | DECLINE |  | ACCEPT | 

## Slide 48: Mechanical Layout of Components Container: Trade & Selection
Presenter: Majlinda Malellari
Reentry Container Chassis |  | Column & Plate Frame |  | Kevlar, Fiberglas & Epoxy Structural Shell | 
-We chose this because: Primary structural support for CanSat Design requirements: impact resistant, workable, lightweight, full enclosure |  |  |  |  | 
Criteria | Weight | Rating | Reason | Rating | Reason
Workability | 30% | 4 | Columns and plastic shell are easily made | 3 | OK for simple shapes
Impact Resistance | 50% | 2 | Columns deform, plastic is brittle | 5 | Kevlar and Fiberglas is impact resistant
Size/Mass | 20% | 3 | Lightweight, multiple plates are heavy | 4 | Kevlar and Fiberglas is dense and has minimum thickness
Total Score | 100% | 3.0 |  | 4.0 | 
Rank |  | 2 |  | 1 | 
Decision |  | Decline |  | Accept | 

## Slide 49: Re-Entry Container Shell
Presenter: Majlinda Malellari
Full View of Container (without paint)
Section View (without paint)

## Slide 50: Mechanical Layout of Components Science Vehicle: Trade & Selection
Presenter: Majlinda Malellari
Science Payload Chassis (shape) |  | Hexagonal |  | Cylindrical | 
We chose this because it will: Increase aerodynamic effect Utilize maximum spacing for components Circular shape provides less stress conentration |  |  |  |  | 
Criteria | Weight | Rating | Reason | Rating | Reason
Strength | 30% | 2 | Stress concentrates on edges | 4 | Cylindrical shape dissipates stress
Drag | 30% | 4 | Fluent simulation shows no differences | 4 | Fluent simulation shows no differences
Component Spacing | 40% | 3 | More spacing | 3 | Reasonable attachment on curved surfaces
Total Score | 100% | 3.0 |  | 3.7 | 
Rank |  | 2 |  | 1 | 
Decision |  | DECLINE |  | ACCEPT | 

## Slide 51: Science Payload Shell
Presenter: Majlinda Malellari
Science Vehicle
Science Vehicle (Section view)

## Slide 52: Mechanical Layout of Components Release Mechanism: Trade & Selection
Presenter: Majlinda Malellari
Retracted (detach from container)
Enforced (connected to the container)
Pivot Release
Release without support plate

## Slide 53: Mechanical Layout of Components Release Mechanism: Trade & Selection
Presenter: Majlinda Malellari
Claw Release
Closed
Open

## Slide 54: Mechanical Layout of Components Release Mechanism: Trade & Selection
Presenter: Majlinda Malellari
Release Mechanism |  | Claw Lock |  | Pivot Release | 
We chose this because: Simple & Efficient Easy to mount and compact |  |  |  |  | 
Description |  | Servo triggered in combination with spring load |  | Servo Triggered, linkage connection within mechanism | 
Criteria | Weight | Rating | Reason | Rating | Reason
Simplicity | 30% | 3 | Many parts | 3 | Many parts.
Easy to Manufacture and Feasibility | 40% | 4 | Few parts to manufactures | 4 | Few parts will be manufactured, most parts will be purchased
Component Spacing & Placement | 20% | 2 | Hard to mount servo and the overall mechanism | 4 | Servo mounted on fiberglass plate
Total Score | 100% | 3.00 |  | 3.70 | 
Rank |  | 2 |  | 1 | 
Decision |  | DECLINE |  | ACCEPT | 

## Slide 55: Material Selections for Descent System: Rotor Hub
Presenter: Majlinda Malellari
Rotor Hub Material |  | Aluminum |  | Nylon | 
Primary attachment point for the blades of the Autorotation Subsystem Must accommodate four blades and fit within a cylinder of 130mm diameter Design requirements: impact resistant, strong, workable, lightweight, |  |  |  |  | 
Criteria | Weight | Rating | Reason | Rating | Reason
Workability | 20% | 3 | More easily machined | 3 | Susceptible to breakage during machining
Strength | 50% | 4 | Low chance of plastic deformation | 3 | Very strong, but less than aluminum
Size/Mass | 30% | 2 | Very dense, heavy | 4 | Lightweight
Total Score | 100% | 3.0 |  | 3.3 | 
Rank |  | 2 |  | 1 | 
Decision |  | Decline |  | Accept | 

## Slide 56: Material Selections for Descent System: Blade Material
Presenter: Majlinda Malellari
Blade System |  | 305 Polyurethane |  | Carbon Fiber | 
Hollow Carbon Fiber material. Strong and light. Test using a statistical approach to determine best overall solution. |  |  |  |  | 
Criteria | Weight | Rating | Reason | Rating | Reason
Rigidity | 20% | 3 | Test result | 4 | Reasonable rigidity and high heat tolerance
Density | 30% | 3 | Test result | 3 | Good
Yield Strength | 20% | 2 | Test result | 3 | Good Tensile strength
Size/Mass | 30% | 2 | Heavy | 4 | Light Weight
Total Score | 100% | 2.5 |  | 3.5 | 
Rank |  | 2 |  | 1 | 
Decision |  | Decline |  | Accept | 

## Slide 57: Material Selections Payload & Container Shells
Material: Resin enforced Kevlar and Fiberglas Fabric
Reasons:
Light weight
Shock force resistance, durability and strength due to woven composition of Kevlar fabric and its high strength to weight ratio
Resin reinforced
Presenter: Majlinda Malellari
Container
Payload

## Slide 58: Container - Payload Interface
58
Presenter: Majlinda Malellari
Servo
Link Couples
Arm
Servo will be attached into a fiberglass plate
Arms will be pushing into the inner surface of container as the servo is originally placed into right position
As the servo is being triggered the Arms will retract inside the Science Vehicle allowing it to detach itself from the container and separate for descent
Note: Support plate for the release mechanism is not included
Arm Cap

## Slide 59: Container - Payload Interface Cont’d
59
Presenter: Majlinda Malellari
Container wall (wireframe display)
Science Vehicle wall (wireframe display)
Slot
(for reinforcing plate)
Servo
Arm support attached to the inner wall of container
Arm support attached to the wall of Payload
Arm
Arm Cap
Arm cap and Arm supports will be 3D printed and the material that will be used ABS plastic
Mechanism support plate
Link Couple
Camera

## Slide 60: Container - Payload Interface Cont’d
60
Presenter: Majlinda Malellari
Additional view of the Pivot Release (Parts indicated on the pervious slide)
Full view of CanSat

## Slide 61: Deployment of Descent Control System
61
Presenter: Majlinda Malellari
The rotor blades will be in a closed position while Science Vehicle is pared with the Container
At separation from container, blades will open and be held on that position due to the spring attachment into the hub-blade interference

## Slide 62: Structure Survivability Trades: Electronics Enclosures and Connections
CanSat 2015 CDR: Team 4996 (Phoenix)
62
Presenter: Majlinda Malellari
Electronics mounted onto PCBs
PCBs mounted to payload via slots enclosed in payload shell
Payload is enclosed in a container

## Slide 63: Structure Survivability Trades: Electronics Mount
CanSat 2015 CDR: Team 4996 (Phoenix)
63
Presenter: Majlinda Malellari
Payload Mounting Plate Material |  | Kevlar Panel |  | PCB | 
Primary structural support for Payload interior components: Electronics, antennae, egg enclosure, etc. 125mm diameter Design requirements: impact resistant, workable, lightweight, full enclosure, withstand force from 30 G’s of acceleration |  |  |  |  | 
Criteria | Weight | Rating | Reason | Rating | Reason
Workability | 20% | 4 | Easily cut to size | 5 | Simplifies layout
Impact Resistance | 50% | 5 | Impact resistant | 4 | Mount brackets will ensure stability
Size/Mass | 30% | 3 | Lightweight | 5 | Very lightweight and eliminates wiring weight
Total Score | 100% | 4.2 |  | 4.5 | 
Rank |  | 2 |  | 1 | 
Decision |  | Decline |  | Accept | 

## Slide 64: Structure Survivability Trades: Descent Control Mount
CanSat 2015 CDR: Team 4996 (Phoenix)
64
Presenter: Majlinda Malellari
Descent Mount
Hub
The mount will be placed inside the Science Vehicle and attached to it via screws.
Blade
Bottom View of the Mount
Shaft

## Slide 65: Structure Survivability Trades: Descent Control Mount (Cont’d)
CanSat 2015 CDR: Team 4996 (Phoenix)
65
Presenter: Majlinda Malellari
Descent Mount
composed of three parts:
  Top Housing
  Bottom Housing
  Ball Bearing
Note: Top shown transparent for better inner view
Top Housing
Ball Bearing
Bottom Housing

## Slide 66: Structure Survivability Trades: Testing
CanSat 2015 CDR: Team 4996 (Phoenix)
66
Presenter: Majlinda Malellari
Testing has not yet been performed to determine if structure and connections can resist 30 Gs of shock and 15 Gs of acceleration.
Electronic plates mounts are planned to be tested under a vibrations test.
Thermal Test will also be performed to ensure survivability of the system in a hot environment.

## Slide 67: Mass Budget (Container)
CanSat 2015 CDR: Team 4996 (Phoenix)
67
Presenter: Majlinda Malellari
Component | Mass per unit (g) | Quantity | Grand Mass (g) | Source/Uncertainties
Chassis | 219.9 | 1 | 209.9 | Estimates
Parachute attachment link | 7.3 | 1 | 7.1 | Estimates
Parachute with hook | 20.6 | 1 | 20.6 | Estimates
Total Container Mass: 247.8 grams |  |  |  | 

## Slide 68: Mass Budget (Payload)
CanSat 2015 CDR: Team 4996 (Phoenix)
68
Presenter: Majlinda Malellari
Component | Mass per unit (g) | Quantity | Grand Mass (g) | Source/Uncertainties
Chassis | 98.16 | 1 | 98.16 | Estimates
Plates | 6.24 | 6 | 37.44 | Estimated
Arm Supports | 0.35 | 2 | 0.7 | Estimated
Arm Caps | 0.13 | 2 | 0.26 | Estimated
Egg Protection System | 20 | 1 | 20 | Measured
PCB | 8.46 | 1 | 8.46 | Estimates
Plate bracket | 1.17 | 9 | 10.53 | Estimates
Spring | 3.85 | 1 | 3.85 | Estimates
Descent Mechanism | 64.54 | 1 | 64.54 | Estimates
Descent Mount | 13.8 | 1 | 13.8 | Estimates
Total Payload Mass: 258.19 grams |  |  |  | 

## Slide 69: Mass Budget (Electronics)
CanSat 2015 CDR: Team 4996 (Phoenix)
69
Presenter: Majlinda Malellari
Component | C or P | Mass per unit (g) | Quantity | Grand Mass (g) | Source/Uncertainties
Arduino Pro Mini | P | 3.8 | 1 | 3.8 | Manufacturer's specs
ADXL345 | P | 2.2 | 1 | 2.2 | Manufacturer's specs
BMP 180 | P | 1.6 | 1 | 1.60 | Manufacturer's specs
XBEE | P | 8.37 | 1 | 8.37 | Manufacturer's specs
Breakout Board | P | 2.03 | 1 | 2.03 | Manufacturer's specs
TMP36 | P | 1.5 | 1 | 1.5 | Manufacturer's specs
Antenna | P | 14 | 1 | 14 | Manufacturer's specs
Battery | P | 60 | 1 | 60 | Measured
Servo | P | 4.7 | 1 | 4.7 | Measured
Total Electronics Mass: 98.2 grams |  |  |  |  | 

## Slide 70: Mass Budget (Summary)
CanSat 2015 CDR: Team 4996 (Phoenix)
70
Presenter: Majlinda Malellari
CanSat Section | Mass (g)
Container | 247.8
Payload (including descent mechanism and descent mount) | 258.19
Electronics | 98.2
Total Mass (without egg) | 604.19

## Slide 71: Communication and Data Handling Subsystem Design
Demetrios Doumas

## Slide 72: CDH Overview
Communication Data Handling components:
Sensors | Role
Arduino Pro Mini 5 volt | Micro Controller
Xbee Series 3 | Radio Transmitter
ADXL345 | Read x, y, z acceleration of the CanSat
BMP180 | Calculate inside temperature and altitude
TMP36 | Calculate Outside temperature.
900MHz 3 dBi Rubber Duck Antenna | Send telemetry data over a far range

## Slide 73: CDH Overview (Continue)
Sensors | Role
Luminosity sensor TSL2561 | Is needed to check rocket deployment
Chronodot | Is needed to fix mission time if a processor reset has happen.
24LC256 EEproms | Store external time from Chronodot

## Slide 74: CDH Overview (Continue)
Sensors | Picture
Arduino Pro Mini 5 volt | 
Xbee Series 3 | 
LSM303DLH 3-Axis Electronic Compass Accelerometer Module Compass Sensor | 
BMP180 | 
TMP36 | 

## Slide 75: CDH Overview (Continue)
Sensors | Picture
900MHz 3 dBi Rubber Duck Antenna | 
Luminosity sensor TSL2561 | 
Chronodot | 
24LC256 EEproms | 

## Slide 76: CDH Changes Since PDR
Changes:
1.) Added the Chronodot and 24LC256 EEproms in case of a processor reset.
2.) Replace the ADXL345 with the LSM303DLH 3-Axis Electronic Compass Accelerometer Module Compass Sensor
The LSM303DLH will help track the cameras movement.

## Slide 77: CDH Requirements
Presenter: Demetrios Doumas
ID | Req. No | REQUIREMENT
CDHR-01 | 21 | During descent, the Science Vehicle shall collect and telemeter air pressure (for altitude determination), outside and inside air temperature, flight software state, battery voltage, and bonus objective data (accelerometer data and/or rotor rate).
CDHR-02 | 22 | The Science Vehicle shall transmit telemetry at a 1 Hz rate.
CDHR-03 | 23 | Telemetry shall include mission time with one second or better resolution, which begins when the Science Vehicle is powered on.
CDHR-04 | 24 | XBEE radios shall be used for telemetry. 2.4 GHz Series 1 and 2 radios are allowed. 900 MHz XBEE Pro radios are also allowed.
CDHR-05 | 25 | XBEE radios shall have their NETID/PANID set to their team number (decimal).
CDHR-06 | 26 | XBEE radios shall not use broadcast mode.
CDHR-07 | 27 | The Science Vehicle shall have a video camera installed and recording the complete descent from deployment to landing. The video recording can start at any time and must support up to one hour of recording.

## Slide 78: CDH Requirements Cont’d
Presenter: Demetrios Doumas
ID | Req. No | REQUIREMENT
CDHR-08 | 28 | The video camera shall include a time stamp on the video. The time stamp must work from the time of deployment to the time of landing.

## Slide 79: Processor & Memory Trade & Selection
Criteria | Weight | Arduino Pro Mini 5V (ATmega328) | Grade | Pro Micro 5V (ATmega32U4) | Grade
Processor speed | 20% | 16MHz | 3 | 16MHz | 3
Data interfaces | 20% | Digital: 14 Analog: 8 PWM: 6 | 4 | Digital: 12 Analog: 10 PWM: 5 | 3
Flash Memory | 20% | 32KB | 3 | 32kB | 3
Size | 20% | 39x18mm (w/ FTDI adapters) | 4 | 33x17.7mm | 5
Cost | 20% | $9.95 | 5 | $19.95 | 4
Weighted Total | 100% |  | 3.8 | Does not need FTDI adapters | 3.6
Presenter: Demetrios Doumas

## Slide 80: Processor & Memory Trade & Selection
Selected Arduino Pro Mini 5V
1.) Cost less than the Pro Micro 5V (ATmega32U4)
2.) Has more Digital interfaces than the Pro Micro 5V (ATmega32U4)

## Slide 81: Real-Time Clock
The flight software on the 5 volt Arduino pro mini will keep track of time throughout the flight time.
The external clock (Chronodot) will be running in parallel.
If the processor resets then the flight state is retrieved from the EEproms and the time from the Chronodot will be saved to mission time.

## Slide 82: Antenna Trade & Selection
Criteria | Weight | SFE Cellular Helical Antenna | Grade | SFE 900MHz Duck Antenna | Grade | HyperLink HG903D-RSP | Grade
Frequency | 30% | 900-1990 MHz | 5 | 900/1800 MHz | 5 | 860-960 MHz | 5
Gain | 20% | 2 dbi | 4 | 2 dbi | 4 | 3 dbi | 3
VSWR | 30% | < 3 | 2 | <1.8 | 5 | <2 | 4
Radiation Pattern H-Plane E-Plane | 20% |  | 4 |  | 3 |  | 4
Weighted Total |  |  | 3.7 |  | 4.4 |  | 4.1
Presenter: Demetrios Doumas

## Slide 83: Antenna Trade & Selection
Selected SFE 900MHz Duck Antenna
1.) Low gain of 2 dbi, which means more coverage on the H-plane.
2.) Has a low voltage standing wave ratio, which means less power loss of the signal coming from the xbee radio transmitter.

## Slide 84: Radio Configuration
The XBee-PRO 900MHz XSC S3B radios will be configured with the XCTU -firmware.
Modem ID will be the Team ID.
When powered on, the XBee will automatically join network. No management needed.
Presenter: Demetrios Doumas

## Slide 85: Telemetry Format
Data Included:
  Team-ID -Mission Time
  Altitude -Outside Temperature
  Inside Temperature -Voltage
  Flight state - X,Y,Z Acceleration
Data format: <TeamID>,<MissionTime>,<Altitude>,<Outside Temperature>,<Inside Temperature>,<Voltage>,<Flight State> <3-AxisAccel(tilt)>
Data rate:
  9600 (bytes per second)
  Continuous transmission
Presenter: Demetrios Doumas

## Slide 86: Electrical Power Subsystem Design
Joel Annenberg

## Slide 87: EPS Overview
Payload:
  9V Battery– power source
  1k ohm voltage divider – for voltage sensing
  TL431 diode - voltage reference for precision voltage sensing
  3V CR1632 lithium coin cell – to power external clock
  LEDs – to verify payload status
Container:
  No electronics in container
Presenter: Joel Annenberg

## Slide 88: EPS Overview Continued
Presenter: Joel Annenberg
Arduino regulated 5V
Sensors:
Accel, Temps, BMP
Power Source
9V
LEDs
XBee regulated 5V
Servo 3-5V
Umbilical cord

## Slide 89: EPS Changes Since PDR
Presenter: Joel Annenberg
Change | Reason
Added 3V coin cell | Required to power the external clock that was added to the electrical system
Added external voltage reference | Increase accuracy of voltage measurement
Power requirements changed | Added more sensors, which led to the consumption of more power

## Slide 90: EPS Requirements
Presenter: Joel Annenberg
ID | Req. No | REQUIREMENT
EPSR-01 | 42 | The Science Vehicle shall include an easily accessible power switch which does not require removal from the Container for access. An access hole or panel in the Container is allowed.
EPSR-02 | 43 | The Science Vehicle must include a battery that is well secured.
EPSR-03 | 44 | Lithium polymer cells are not allowed due to being a fire hazard.
EPSR-04 | 45 | Alkaline, Ni-MH, lithium ion built with a metal case, and Ni Cad cells are allowed.

## Slide 91: Electrical Block Diagram (Payload)
An externally accessible switch will be installed between the 9V battery and the microcontroller.
A power umbilical cord will be attached to the microcontroller to allow for testing
LEDs will be externally visible for status verification (for testing only)
Sensors are all rated for use with 5V power (some regulate voltage down to 3.3V).
Presenter: Joel Annenberg
Arduino regulated 5V
Sensors:
Accel, Temps, BMP
Power Source
9V
LEDs
XBee regulated 5V
Servo 3-5V
Umbilical cord

## Slide 92: Electrical Block Diagram: Container
There will be no container electronics, as all of the required electronics will be contained in the payload.
Presenter: Joel Annenberg

## Slide 93: Power Source Trade & Selection (Payload)
Presenter: Joel Annenberg
Criteria | Weight | Energizer Advanced | Grade | Duracell Coppertop | Grade
Weight | 75% | 33.9 g | 4 | 45 g | 2
Price | 25% | $5.99 | 3 | $3.99 | 4
Weighted Total | 100% |  | 3.75 |  | 2.50

## Slide 94: Power Source Summary
Payload Power Source:
  Energizer Advanced Lithium Alkaline
  9V @ 150mA
  46.4 x 26.5 x 17.5 mm
  33.9g / unit
  $5.99 / unit
  Powerful, light, reliable
Container Power Source:
  None
Presenter: Joel Annenberg

## Slide 95: Payload Power Source Selection and Design
Power will be generated from 1 Energizer Advanced Lithium-Alkaline 9V Battery (9V @ 150 mA min.)
Supplies ample power and is lighter and more reliable than traditional 9V batteries.
Total power consumption will be 606.48 mW out of a total availability of 1350 mW.
Presenter: Joel Annenberg

## Slide 96: Power Budget (Payload)
Components | Power Consumed | Duty Cycle | Source | Total Power Consumed
Arduino | 15.8 mW | 14% | Measurement | 2.6 mWh
Xbee Pro XSC 900MHz (P.L.2) | 126.7 mW | 14% | Measurement | 20.7 mWh
Accelerometer & Magnetometer LSM303 | 0.363 mW | 14% | Data Sheet | 0.061 mWh
Barometer BMP180 | .05 mW | 14% | Data Sheet | 0.008 mWh
Servo | 396 mW | ~0% | Measurement | 0.11 mWh
LED | 66 mW | 14% | Data Sheet | 11 mWh
Temperature Sensor TMP36 | 0.25 mW | 14% | Data Sheet | 0.042 mWh
Luminosity Sensor TSL2591 | 1.32 mW | 14% | Data Sheet | 0.22 mWh
 |  |  | Total: | 100.62 mWh
 | Power Available |  |  | Total Power Supplied
9V Battery @ 150 mA | 1350 mW | 100% |  | 225 mWh
Presenter: Joel Annenberg
Est. Mission Duration: 4200s Est. Powered Time: 600s

## Slide 97: Flight Software (FSW) Design
Demetrios Doumas

## Slide 98: Flight Software

## Slide 99: FSW Overview
Language
  C programming language
Development Environment
  Arduino software (free open source)
FSW Tasks
  Record, store and transmit data.
  Activate release mechanism at designated altitude.
  Camera record descent

## Slide 100: FSW Requirements
Presenter: Demetrios Doumas
ID | Req. No | REQUIREMENT
FSWR-01 | 10 | The Container or Science Vehicle shall include electronics and mechanisms to determine the best conditions to release the Science Vehicle based on stability and pointing. It is up to the team to determine appropriate conditions for releasing the Science Vehicle.
FSWR-02 | 21 | During descent, the Science Vehicle shall collect and telemeter air pressure (for altitude determination), outside and inside air temperature, flight software state, battery voltage, and bonus objective data (accelerometer data and/or rotor rate).
FSWR-03 | 22 | The Science Vehicle shall transmit telemetry at a 1 Hz rate.
FSWR-04 | 23 | Telemetry shall include mission time with one second or better resolution, which begins when the Science Vehicle is powered on.
FSWR-05 | 27 | The Science Vehicle shall have a video camera installed and recording the complete descent from deployment to landing. The video recording can start at any time and must support up to one hour of recording.
FSWR-06 | 28 | The video camera shall include a time stamp on the video. The time stamp must work from the time of deployment to the time of landing.

## Slide 101: FSW Requirements
Presenter: Demetrios Doumas
ID | Req. No | REQUIREMENT
FSWR-07 | 40 | The CanSat flight software shall maintain and telemeter a variable indicating its operating state. In the case of processor reset, the flight software shall re-initialize to the correct state either by analyzing sensor data and/or reading stored state data from non-volatile memory. The states are to be defined by each team. Example states include: PreFlightTest(0), LaunchWait(1), Ascent(2), RocketDeployment(3), Stabilization(4), Separation(5), Descent(6), and Landed(7).

## Slide 102: CanSat FSW State Diagram
States | Conditions | Sensors
Pre-FlightTest (0) | CanSat Boot | External switch
LaunchWait(1) | Passes Pre-FlightTest | 
Ascent(2) | Change in Altitude is >0 | Accelerometer @ 1Hz, and Pressure Sensor @ 1Hz
Rocket Deployment(3) | Cansat is expose to light | Luminosity sensor TSL2561 @ 1Hz
Stabilization(4) | Accelerometer tilt is closer to zero. | Accelerometer @ 1Hz
Separation(5) | Altitude has reached 300 meters | Pressure Sensor @ 1Hz
Descent(6) | Change in Altitude is <0 | Accelerometer @ 1Hz
Landed(7) | Altitude at ground level | Accelerometer @ 1Hz
Presenter: Demetrios Doumas

## Slide 103: CanSat FSW State UML-Diagram

## Slide 104: Software Development Plan
A common CanSat problem is late software development
Present a slide describing the plan for software development and plans to reduce the risk of late software development
Include:
  Prototyping and prototyping environments
  Software subsystem development sequence
  Development team
  Test methodology
Discuss progress since PDR

## Slide 105: Software Development Progress
Progress:
1.) Calculate all required telemetry data.
2.) Able to transmit telemetry data.

## Slide 106: Software Development Plan

## Slide 107: Ground Control System (GCS) Design
Demetrios Doumas

## Slide 108: GCS Overview
Telemetry data flow:
Laptop
Xbee Series 3
Quad-Band Omni-directional Antenna
FG16397
Cansat

## Slide 109: GCS Requirements
ID | Req. No | REQUIREMENT
GCSR-01 | 24 | XBEE radios shall be used for telemetry. 2.4 GHz Series 1 and 2 radios are allowed. 900MHZ XBEE Pro radios are also allowed.
GCSR-02 | 25 | XBEE radios shall have their NETID/PANID set to their team number.
GCSR-03 | 26 | XBEE radios shall not use broadcast mode.
GCSR-04 | 32 | Each team shall develop their own ground station.
GCSR-05 | 33 | All telemetry shall displayed in real time during descent.
GCSR-06 | 34 | All telemetry shall be displayed in engineering units (meters, meter/sec, Celsius, etc).
GCSR-07 | 35 | Teams shall plot data in real time during flight on ground station computer.
GCSR-08 | 36 | The ground control station shall include one laptop computer with a minum of two hours of battery operation, XBEE radio and a hand held or table top Antenna.
Presenter: Demetrios Doumas

## Slide 110: GCS Requirements Cont’d
ID | Req. No | REQUIREMENT
GCSR-09 | 37 | The ground station shall be portable so the team can be positioned at the ground station operation site along the flight line. AC power will not be available at the ground station operation site.
Presenter: Demetrios Doumas

## Slide 111: GCS Antenna
Discussion of the selection of the GCS antenna
Include:
  Antenna placement and coverage
    Diagram is recommended
  Antenna height and mounting strategy
    Launch day construction
  Distance link predictions and margins
  Screen shot of ground control software in operation

## Slide 112: Screen shot of ground control software in operation

## Slide 113: GCS Antenna Trade selection
Criteria | Quad-Band Omni-directional Antenna FG16397 | Hyper Link Yagi HG903YE | Die Cast Grid Antenna
Gain: | 1dBi | 3dBi | 15dBi
Type: | Omni Directional | Directional | Directional
Cost: | $100 | $30 | $ 90
Weight: | 0.844 lbs | 1.5 lbs | 6.55 lbs
Polarization: | Linear vertical | Horizontal or vertical | Horizontal or vertical
Frequency: | 900MHz | 900MHz | 824~960 Hz
Presenter: Demetrios Doumas

## Slide 114: Distance Link and Predictions
The antenna will be mounted as a tabletop antenna during the launch day.
The selected antenna radiation pattern is:
Azimuth
Elevation
Presenter: Demetrios Doumas
Elevation Beamwidth at Half-Power: 90 degrees
Azimuth Beamwidth at Half-Power: 360 degrees
The Omni-directional Antenna
FG16397 was chosen because of its 360 degree coverage in the horizontal plane.

## Slide 115: GCS Software
Telemetry display screen shots
Commercial off the shelf (COTS) software packages used
Real-time plotting software design
Data archiving and retrieval approach
Command software and interface
Progress since PDR
Testing

## Slide 116: GCS Software
Commercial off the shelf (COTS) software packages used:
Matlab 2013: Creating a Graphic User Interface (GUI).
Arduino: Diagnostic purposes for checking serial port readings.
Presenter: Demetrios Doumas

## Slide 117: GCS Software: Flow Chart
Real-time plotting software design:
Presenter: Demetrios Doumas

## Slide 118: GCS Software: Data archiving and retrieval approach
Data archiving Steps:
1.) Read data from serial port every 1 Hz.
2.) Save the data in an excel file.
3.) Plot current data on the screen
4.) Repeat
Presenter: Demetrios Doumas

## Slide 119: GCS Software Interface
Presenter: Demetrios Doumas

## Slide 120: GCS Software: Telemetry
Telemetry data recording and media presentation:
Payload Telemetry Data:
Team id, mission time, alt sensor, outside temperature, inside temperature, voltage, flight state, X, Y, and Z.
X, Y, and Z are accelerometer readings.
Presenter: Demetrios Doumas

## Slide 121: Progress Since PDR
Radio communication established between the GCS software and cansat prototype.
GCS software finished

## Slide 122: Testing
Indoors:
The electronics are connected directly to the laptop, where the GCS software is reading the data.
Also, test the flight states operation by doing an altitude test inside an elevator.
Outdoors:
The CanSat will be placed in a rocket (similar to the CanSat competition rocket) and released in an open area in Pennsylvania.
Antenna Testing, whether data is being received with the Arduino software

## Slide 123: CanSat Integration and Test
Sakif Chowdhury

## Slide 124: CanSat Integration and Test Overview
Flight Software
  Test Navigation Software
Mechanical Systems
  Drop test and Vibration Test
  Temperature Test
Sensors
  Individual testing for reliability, accuracy, and precision of each sensor
Communications and Data Handling
  1 mile line of sight test
  Test communication systems
  Tests data analysis conducted at ground station
Electrical Power Systems
  Measure estimated necessary power
Presenter: Sakif Chowdhury

## Slide 125: CanSat Assembly
Assembly of primary components of CanSat:
Container will be housing the Science Vehicle
Science Vehicle is connected to the reentry container via the release
Mechanism
The Electronics Plates are slotted on the upper section on the Payload and the Egg Protection is placed on the bottom section along with the camera.
Presenter: Sakif Chowdhury
Container
Descent System
Science Vehicle
PCB
Release Mechanism

## Slide 126: Integration and Testing Goals
Current Goals
  To be able to complete most of the manufacturing in April in order to perform proper testing
  Complete a proto type of the CanSat for fully integrated testing
  Analyze tests thoroughly in order to make changes/improvements
  To be able to make sufficient improvements while meeting competition requirements
Presenter: Sakif Chowdhury

## Slide 127: Tests and Scheduled Dates
Test Type | Brief Description | Reason | Test Date
Drop Test | Shock Absorbance measurement using Kevlar thread | To observe the resistivity of fracture of the mechanical body and release mechanism | April 9th 2015
Wind Tunnel | Apply wind flow through mechanical structure | To observe the functionality of descent system and behavior of blades due to air flow | April 13th 2015
Thermal | Use Thermal Chamber on electronics at various temperatures | To observe the capability of electronics to withstand high temperatures and stability of mechanical design | April 6th 2015
Vibration Analysis | Apply vibrational forces up to 29 G forces | To measure the stability of electronics and analyze stress on mechanical system | April 10th 2015
Presenter: Sakif Chowdhury

## Slide 128: DCS Subsystem Testing Overview
Test | Reason | Passing Criteria
Wind Tunnel | Correlate simulation data with experimental values for descent rate estimates | Terminal angular velocity and forces measured close to approximated data
Shock (Blades) | Determine effectiveness of blade attachment mechanism | Blades remain attached to rotor with no damage incurred
Shock (Parachute) | Determine effectiveness of parachute cord | Cord does not break, parachute remains intact

## Slide 129: Mechanical Subsystem Testing Overview
Test | Reason | Passing Criteria
Container and Payload shell | Determine survivability | Survive landing impact
Release Mechanism | Determine effectiveness of mechanism | Payload deploys from Container with ease
Egg Protection System | Determine effectiveness of system | Egg survives landing

## Slide 130: CDH Subsystem Testing Overview
Test | Reason | Passing Criteria
XBEE Communications | Determine effectiveness of the communication between XBEE transmitter and receiver | Data is transmitted and received without interference

## Slide 131: FSW Code Testing
Test | Reason | Passing Criteria | Date
Container Code | Debug and remove possible glitches | Transmits necessary data and releases payload as programmed | April 6, 2015
Payload Code | Debug and remove possible glitches | Transmits necessary data | April 6, 2015
Presenter: Sakif Chowdhury

## Slide 132: GCS Testing Overview
Test | Reason | Passing Criteria
Antenna | Determine maximum effective range | Works within 1 mile radius
Presenter: Sakif Chowdhury

## Slide 133: Mission Operations & Analysis
Ruben Perez

## Slide 134: Overview of Mission Sequence of Events
Presenter: Ruben Perez
8:00am-12:00pm
Launch preparations
1:00pm
Launch will start
Check in
Obtaining the Science vehicle egg
Assemble antennas and ground station
Perform Final CanSat Tests and reparations
Data is recovered
CanSat is submitted
12:00pm-1:00pm
Any Ground Station problem are worked

## Slide 135: Overview of Mission Sequence of Events
Presenter: Ruben Perez
Mission Control Officer:
CanSat Crew:
Ground Station Crew:
Recovery Crew:
Ruben Perez
Patrick Guillaume & Joel Annenberg
Maria Caceres & Majlinda Malellari
Demetrios Doumas

## Slide 136: Antenna Construction and Ground Station Set Up
Ground station computers will be set up and connected to antenna in preparation for mission.
Any glitches will be sorted out before launch
Presenter: Ruben Perez

## Slide 137: Field Safety Rules Compliance
The Mission Operation Manual from previous year will be used with changes.
Mission Operation Manual will be broken down into two part.
  Necessary procedures are imbedded into the Competition Operations and Launch Day Sequence of Events
  Manual will contain major tasks to be executed by each team for the time intervals mentioned above
Part I- General Mission Operation that includes CanSat Integration, launch Preparation, launch and removal procedures.
  The manual will be organized into three launch-day time intervals
  8AM-12PM
  12-1PM
  1PM- MISSION END
An example of procedure is provided in the next slide for Part I and Part II
Presenter: Ruben Perez

## Slide 138: Field Satefy Compliance Con’t

## Slide 139: Field Safety Rules Compliance
Part II- CanSat Preparation & Test and Ground Station Setup
The CanSat preparation procedures still needs to be written.
Presenter: Ruben Perez

## Slide 140: CanSat Location and Recovery
The container and Payload will be painted neon pink.
The school address will be written on the Container and Payload
Presenter: Ruben Perez

## Slide 141: Mission Rehearsal Activities
Ground system radio link check procedure
  Two xbee adapater were used. One was connected to the computer and the other connected to the electronics. Testing was done in order to determine if data was being transmitted into the FSW and that was successful.
Loading the egg payload
  The egg will be placed inside a cardboard container and surrounded by foam on the inside. This has been tested by dropping the egg and seeing that it survives the fall.
Powering on/off the CanSat
  The use of a switch and an LED light to determine if the CanSat is on/off.
Presenter: Ruben Perez

## Slide 142: Mission Rehearsal Activities
Launch configuration preparations
  A rocket similar to the one that is use in the competition will be made and used to test the placement of the CanSat.
Loading the CanSat in the launch vehicle
  The size of the max inner tubing of the container will be bought in order to test that the payload fits perfectly.
Telemetry processing, archiving, and analysis
  When the electronics are all connected to the PCB a test will be done to determine if the electronics are working properly and transmitting/receiving data.
Recovery
  Members of this team will practice keeping track of the cansat visually (with binoculars) during our fully integrated test
Presenter: Ruben Perez

## Slide 143: Requirements Compliance
Ruben Perez

## Slide 144: Requirements Compliance Overview
Design of the CanSat complies to most of the requirements.
Those that remain depend on testing which will be done in the future
The following Color Code was used:
    Green: Full Compliance
    Yellow: Partial Compliance (tests not completed yet but planned)
    Red: No Compliance
Presenter: Ruben Perez

## Slide 145: Requirements Compliance
Presenter: Ruben Perez
Req # | Requirement | Compliance | See Slide | Comments
1 | Total mass of the CanSat (container and payload) shall be 600 grams +/- 10 grams without the egg. | COMPLY | 67 | 
2 | The Science Vehicle shall be completely contained in the Container. Shall not extend beyond the container. | COMPLY | 42 | 
3 | Container shall fit in the envelope of 125 mm x 310 mm including the container passive descent control system. Tolerances are to be included to facilitate container deployment from the rocket fairing. | COMPLY | 13, 15 | 
4 | The Container shall use a passive descent control system. | COMPLY | 26 | 
5 | The container shall not have any sharp edges to cause it to get stuck in the rocket fairing section. | COMPLY | 15 | 
6 | The container shall be a florescent color, pink or orange | COMPLY | 45 | 
7 | The rocket air frame shall not be used to restrain any deployable parts of the CanSat. | COMPLY | 15 | 
8 | The rocket airframe shall not be used as part of the CanSat operations. | COMPLY | 15 | 
9 | The CanSat (container and payload) shall deploy from the rocket fairing section. | COMPLY | 15 | 

## Slide 146: Requirements Compliance Cont’d
Presenter: Ruben Perez
Req # | Requirement | Compliance | See Slide | Comments
10 | The Container or Science Vehicle shall include electronics and mechanisms to determine the best conditions to release the Science Vehicle based on stability and pointing. | COMPLY | 13,18, 89 | 
11 | The science Vehicle shall use a helicopter recovery system. The blades must rotate and not use any fabric or other material between the blades. | COMPLY | 26,3134 | 
12 | All descent control device attachments shall survive 50 Gs of shock. | COMPLY |  | 
13 | All descent control devices shall survive 50 Gs of shock | COMPLY |  | 
14 | All electronic components shall be enclosed and shielded from the environment with the exception of sensors. | COMPLY |  | 
15 | All structures shall be built to survive 15 Gs acceleration. | COMPLY |  | 
16 | All structures shall be built to survive 30 Gs of shock | COMPLY |  | 
17 | All electronics shall be hard mounted using proper mounts such as standoffs, screws, or high performance adhesives. | COMPLY | 59 | 

## Slide 147: Requirements Compliance Cont’d
Presenter: Ruben Perez
Req # | Requirement | Compliance | See Slide | Comments
18 | All mechanisms shall be capable of maintaining their configuration or states under all forces. | COMPLY |  | 
19 | Mechanisms shall not use pyrotechnics or chemicals. | COMPLY | 11,12 | 
20 | Mechanisms that use heat (e.g., chrome wire) shall not be exposed to the outside environment to reduce potential risk of setting vegetation on fire. | COMPLY | 11,12 | 
21 | During descent, the science Vehicle shall collect and telemeter air pressure, outside and inside air temperature, flight software state, battery voltage, and bonus objective. | COMPLY |  | 
22 | The Science Vehicle shall transmit telemetry at a 1 Hz rate. | COMPLY |  | 
23 | Telemetry shall include mission time with one of the second or better resolution, which begins when the Science Vehicle is powered on. | COMPLY |  | 
24 | XBEE radios shall be used for telemetry. 2.4 GHz Series 1 and 2 radios are allowed. 900 MHz XBEE Pro radios are also allowed | COMPLY | 69,75 | 
25 | XBEE radios shall have their NETID/PANID set to their team number. | COMPLY | 75 | 

## Slide 148: Requirements Compliance Cont’d
Presenter: Ruben Perez
Req # | Requirement | Compliance | See Slide | Comments
26 | XBEE radios shall not use broadcast mode | COMPLY | 75 | 
27 | The Science Vehicle shall have a video camera installed and recording a complete descent from deployment to landing. | COMPLY | 22 | 
28 | The video camera shall include a time stamp on the video. | COMPLY | 22 | 
29 | The descent rate of the Science Vehicle shall be less than 10m/s and greater than 4m/s. | COMPLY | 40 | 
30 | During Descent , the video camera must not rotate. | COMPLY |  | 
31 | Cost of the CanSat shall be under $1000. Ground support and analysis tools are not included in the cost. | COMPLY | 134 | 
32 | Each team shall develop their own ground station | COMPLY | 95, | 
33 | All telemetry shall be displayed in real time during descent. | COMPLY | 102,103 | 
34 | All telemetry shall be displayed in engineering units (meters, meters/sec, Celsius, etc.) | COMPLY | 104 | 
35 | Teams shall plot data in real time during flight. | COMPLY | 102,103 | 

## Slide 149: Requirements Compliance Cont’d
Presenter: Ruben Perez
Req # | Requirement | Compliance | See Slide | Comments
43 | The Science Vehicle must include a battery that is well secured. | COMPLY |  | 
44 | Lithium polymer cells are not allowed due to being a fire hazard. | COMPLY | 82 | 
45 | Alkaline, Ni-MH, lithium ion built with a metal case, and Ni-Cad cells are allowed. | COMPLY | 82 | 
46 | The Science Vehicle and Container must be subjected to the drop test. | COMPLY |  | 
47 | The Science Vehicle and Container must e subjected to the vibration test. | COMPLY |  | 
48 | CanSat Vehicle and Container must be subjected to the thermal test. | COMPLY |  | 
49 | Environmental test results must be documented and submitted to the judges at the flight readiness review. | COMPLY |  | 

## Slide 150: Management
Ruben Perez

## Slide 151: Status of Procurements
Part | Quantity | Order Status
Luminosity Sensor TSL2591 | 1 | Ordered
Presenter: Ruben Perez
All other electronic components have been ordered .

## Slide 152: CanSat Budget – Electrical
Electrical(Payload) | Cost | Cost Type | Reused?
Arduino Pro Mini- 5.0V | $9.95 | Actual | New
BMP 180 | $9.95 | Actual | New
TMP 36 | $1.50 | Actual | New
XBEE 900 MHz | $53.69 | Actual | New
Keychain Camera | $24.99 | Actual | New
LSM303 | $14.95 | Actual | New
XBEE Adapter | $9.95 | Actual | New
Data Logger | $24.95 | Actual | New
TSL2591 | $6.95 | Actual | New
PCBs | $60 | Estimate | New
900 MHz 3 dBi Rubber Duck Antenna | $12.43 | Actual | New
Presenter: Ruben Perez

## Slide 153: CanSat Budget – Electrical
Presenter: Ruben Perez
Electrical(Payload) | Cost | Cost Type | Reused?
9V Battery | $5.99 | Actual | New
Luminosity sensor TSL2591 | $6.95 | Actual | New
Chronodot | $17.50 | Actual | New
24LC256 EEproms | $1.95 | Actual | New
Total | 261.61 |  | 

## Slide 154: CanSat Budget – Other Costs
Presenter: Ruben Perez
Electrical | Cost
Payload | $261.61
Miscellaneous (Replacing Damaged Components) | $50
Total | $311.61

## Slide 155: CanSat Budget – Mechanical
Mechanical | Cost | Cost Type | Reused?
Miniature 12L14 Drive Steel Shaft | $4.76 | Actual | New
Rigid HDPE Polyethylene Rod | $50.69 | Actual | New
Aluminum Blind Rivet with Aluminum Mandre | $7.01 | Actual | New
Fabric Snaps | $5.57 | Actual | New
Lightweight Aluminum Socket Head Cap Screw (4-40 Thread, 1/4" Length) | $9.71 | Actual | New
Lightweight Aluminum Socket Head Cap Screw (4-40 Thread, 1/2" Length) | $9.71 | Actual | New
4-40x3/16" Nylon Female Plastic Ball Linkages | $5.99 | Actual | New
Easy Clean Mold Release for Urethanes | $29.95 | Actual | New
Presenter: Ruben Perez

## Slide 156: CanSat Budget – Mechanical Cont’d
Mechanical | Cost | Cost Type | Reused?
302 Stainless Steel Cut-to-Length Compression Spring 20" Length, .312" OD, .035" Wire Diameter | $4.70 | Actual | New
Bi-directional E-Glass | $26.35 | Actual | New
Woven Fiberglass Tape | $7.00 | Actual | New
Kevlar and hybrid Sample Pack | $14.95 | Actual | New
Kevlar-Twill Weave Fabric | $153.95 | Actual | New
2120 Epoxy Hardner | $44.95 | Actual | New
Parting Wax | $10.25 | Actual | New
Release Wedge (Think Flexible) | $3.45 | Actual | New
Yellow Sealant Tape | $7.95 | Actual | New
Miscellaneous | $50 | Estimated | N/A
Total | $446.94 |  | 
Presenter: Ruben Perez

## Slide 157: CanSat Budget – Other Costs
Presenter: Ruben Perez
Type of Components | Cost
Electrical | $311.61
Mechanical | $446.94
Total | $758.55

## Slide 158: Total Competition Budget
Items | Cost | Cost type
CanSat | 759.55 | Estimated
Airfare | $1,855.00 | Estimated
Baggage | $250.00 | Estimated
Hotel | $722.14 | Estimated
Car Rental – Enterprise | $457.17 | Estimated
Total Expenditures | $4042.86 | 
Presenter: Ruben Perez

## Slide 159: Program Schedule Table 1/3
Presenter: Ruben Perez
Task | Start Date | Duration(Days) | End Date
Presentations |  |  | 
First Draft PDR | 1-9-2015 | 20 | 1-28-2015
Final Draft PDR | 1-28-2015 | 4 | 1-31-2015
PDR Submission | 2-1-2015 | 1 | 2-1-2015
First Draft CDR | 2-23-2015 | 19 | 3-13-2015
Final Draft CDR | 3-16-2015 | 10 | 3-25-2015
CDR Submission | 3-31-2015 | 1 | 3-31-2015
Design |  |  | 
Reentry Container | 1-5-2015 | 2 | 1-9-2015
Science Payload | 1-12-2015 | 24 | 1-16-2015
Release Mechanism | 1-16-2015 | 16 | 1-22-2015
Preliminary Solid Model | 1-5-2015 | 18 | 1-22-2015
Software/Code |  |  | 
Electronic Code | 1-5-2015 | 18 | 1-22-15
Flight Software | 2-16-2015 | 21 | 3-9-15
Matlab code for fan blade sim | 11-10-2014 | 26 | 12-5-14

## Slide 160: Program Schedule Table 2/3
Presenter: Ruben Perez
Task | Start Date | Duration(Days) | End Date
Budget |  |  | 
Funding Proposal | 10-30-2015 | 9 | 1-22-15
Purchasing Materials | 3-9-2015 | 3 | 3-11-2015
Tests |  |  | 
Test electronic Components | 1-12-2015 | 11 | 1-23-2015
Blade Simulation | 1-15-2015 | 14 | 1-28-2015
Wind tunnel blade test | 3-24-2015 | 7 | 3-30-2015
Thermal test | 4-3-2015 | 1 | 4-3-2015
Vibration test | 4-3-2015 | 1 | 4-3-2015
Drop test |  |  | 
Manufacture |  |  | 
Manufacture Reentry Container | 2-17-2015 | 7 | 2-23-2015
Manufacture rotor system | 2-23-2015 | 3 | 2-25-2015
Manufacture Science Payload | 2-25-2015 | 9 | 3-5-2015
Manufacture release mechanism | 3-1-2015 | 16 | 3-16-2015
3D Print blade Model | 3-5-2015 | 1 | 3-5-2015

## Slide 161: CanSat Gantt Chart 3/3
Presenter: Ruben Perez
Task | Start Date | Duration(Days) | End Date
Manufacture Blade Mold | 3-11-2015 | 3 | 3-13-2015
Manufacture blades | 3-16-2015 | 8 | 3-23-2015

## Slide 162: CanSat Gantt Chart 1/2
Presenter: Ruben Perez
Chart: 
| Reentry Container | Science Payload | Funding Proposal | Release mechanism | Matlab Code Fanblade Sim | Preliminary Solid Model | First Draft PDR | Test Electronic components | Electronic Code | Blade Simulation | Final Draft PDR | PDR Submision | Manufacture Science Payload | Flight Software | First Draft CDR | 3D Print blade Model
Start Date | 41935 | 41936 | 41942 | 41942 | 41953 | 42009 | 42013 | 42016 | 42019 | 42019 | 42032 | 42036 | 42051 | 42055 | 42058 | 42060
Duration | 2 | 24 | 9 | 16 | 26 | 18 | 20 | 11 | 18 | 14 | 4 | 1 | 9 | 48 | 19 | 3

## Slide 163: CanSat Gantt Chart 2/2
Presenter: Ruben Perez
Chart: 
| Purchased Materials | Final Draft CDR | Manufacture rotor system | CDR Submission | Wind tunnel blade test 1 | Cansat Integration testing | Manufacture release mechanism | Thermal test | Manufacture Blade Mold | Drop test | Manufacture Reentry container | Vibration test | Manufacture blades | Wind tunnel blade test 2
Start Date | 42072 | 42079 | 42086 | 42094 | 42093 | 42095 | 42096 | 42100 | 42101 | 42103 | 42103 | 42104 | 42110 | 42118
Durtaion | 3 | 14 | 5 | 1 | 5 | 16 | 6 | 1 | 9 | 1 | 4 | 1 | 8 | 7

## Slide 164: Conclusions
Ruben Perez

## Slide 165: Shipping and Transportation
Presenter: Ruben Perez
CanSat hardware will be transported with the team to Burkett.
  Hardware will be checked-in at the time of arrival in the airport.
  They will be carry-on items to prevent loss and damage.
Alternative: Shipping via delivery service
  UPS/FedEx ground shipping.

## Slide 166: Conclusions
Presenter: Ruben Perez
Flight Software status
  In progress
Testing to Complete
  Environmental Testing
Major unfished work
  PCB
  Manufacturing Blades
Major accomplishments
  Mold for re-entry container
  All remainder materials have been bought

## Slide 167: Conclusions Cont’d
Presenter: Ruben Perez
Due to delay in acquiring materials because of funding there has been a setback.
Potential Challenges
If we keep on having delays, this will cause problems towards completing the CanSat.
Manufacturing the blades because we have never done our own.